DisplayPort MST:
4K and laptop dock fail?
David Airlie
LCA 2015
Red Hat, Brisbane

---
How did I get here?
[Speaker Notes: RH IT lenovo t440s]

---
History of Display Technologies
[Speaker Notes: VGA, DVI, HDMI, DisplayPort]

---
History of Display Technologies
[Speaker Notes: VGA, DVI, HDMI, DisplayPort]

---
History of Display Technologies
[Speaker Notes: VGA, DVI, HDMI, DisplayPort]

---
History of Display Technologies
[Speaker Notes: VGA, DVI, HDMI, DisplayPort]

---
History of Display Technologies
[Speaker Notes: VGA, DVI, HDMI, DisplayPort]

---
DisplayPort
Tx
Rx
Main Link
(1, 2, 4 lanes)
AUX CH
Hot Plug (HPD)
1 lane = 540MB/s (1.2 HBR), 270MB/s, 162MB/s
AUXCH – 1MB/s – Fast AUXCH 675 MB/s (DP 1.2)

---
Single Stream Transport
(DP 1.1 or SST Mode)
[Speaker Notes: DP/DP Legacy converters VGA/ DVI / HDMI/ active vs passive (not really seen) Repeaters/replicators/switches]

---
AUX CH
[Speaker Notes: Control channel Native auxch for DPCD access Register space on device, Read/write register space Legacy i2c transport For EDID, DDC-CI etc.]

---
Multi-Stream Transport
[Speaker Notes: Virtual channels Mapped into link transport units (TU) Sideband msgs over AUXCH DPCD register space contains 4 blocks UP request + reply DOWN request + reply Broadcast msgs]

---
MST Topology
Source #1
Source #2
0
0
0
Branch 1
2
0
1
1
Branch 2
0
Branch 4
2
0
2
Sink 3
0
Branch 3
0
Branch 5
1
1
2
2
0
0
0
0
Sink 5
Sink 1
Sink 2
Sink 4
Sink 1 – 0.2.2.1 relative to Source 2
[Speaker Notes: GUID 16 bytes via DPCD Must match USB hub in same device RAD (Relative Address)]

---
Payload/Bandwidth Management
- 63 slots
- Payload Bandwidth Number
  - 1 lane @ 162 – 3 PBN	per slot
  - 4 lane @ 540 – 40 PBN per slot
- 1920x1200@60Hz-30bpp
  - 689 PBN

---
MST Protocol
- LINK_ADDRESS
  - Address discovery
- CONNECTION_STATUS_NOTIFY
- RESOURCE_STATUS_NOTIFY
  - Change in topology
- ENUM_PATH_RESOURCES
- ALLOCATE_PAYLOAD
- CLEAR_PAYLOAD_ID_TABLE
  - Payload management

---
MST Protocol
- REMOTE_DPCD_READ
- REMOTE_DPCD_WRITE
  - Remote device DPCD access
- REMOTE_I2C_READ
- REMOTE_I2C_WRITE
  - Remote device i2c access
- POWER_UP_PHY
- POWER_DOWN_PHY
  - Remote device power control

---
Laptop Docks

---
MST Hubs

---
4K Monitors
[Speaker Notes: Single Stream Multi-stream]

---
Monitor Tiling
DisplayID v1.3
[Speaker Notes: EDID replacement Or EDID enhancement]

---
Vendor HW support
[Speaker Notes: Intel Haswell ULX/ULT AMD Radeonhd 6000 – nothern islands nvidia GeForce 6000, nvD9, Kepler Haswell ULX/ULT clock restrictions]

---
Driver Status
[Speaker Notes: Intel 915 Amd radon Nouveua Fglrx/nvidia]

---
X.org
Desktop Environments
[Speaker Notes: Randr 1.5 Monitor Tiling property passthrough Mutter Gtk]

---
Future fun
5K - (5120 x 2880)
DP 1.3 (8.1GBps)
FreeSync

---
My Desk/Questions?