Codec 2 at 450 bit/s
- Codec 2
- Digital Voice over High Frequency (HF) Radio
- The Mission
- Why HF is Hard
- How Analog Does it
- Demo

---
Codec 2
- Open source, low bit rate
- 3200 to 1200 bit/s
- Speech only
- Digital radio applications

---
Digital Voice over HF Radio
A/D
codec2
enc
FEC
enc
mod
mic
HF/VHF
radio
D/A
codec2
dec
FEC
dec
demod
spkr

---
The Mission
- HF: no infrastructure, 1000's of km
- Make Digital Voice work better than Analog
- Over HF channels
- Negative channel SNRs
- This is hard
- But open source makes it easier!

---
Analog and Digital Voice
- Analog has lots of redundancy, Digital has some “global” bits
- Different bits have different importance
- Memory/error propagation
- Gradual decrease in quality with SNR
- Analog applies power intelligently.....
- Power distributed in freq and time

---
My Approach
- In bad HF channels using Analog........
- We yell, repeat ourselves, use the phonetic alphabet
- But … the message gets through
- This is like lowering the bit rate of the information
- We are allocating more power to each letter
- VK5DGR - Victor Kilo Five Delta Golf Romeo
- Human FEC

---
My Approach
- The Digital equivalent is lowering the codec bit rate
- Lower speech quality to the edge of intelligibility
- OK to repeat ourselves
- OK if speech quality is low
- Lower bit rate means more power per bit
- Better chance of bit getting through

---
Demo
- Original
- Codec 2 at 1300 bit/s
- Codec 2 at 450 bit/s
- -5 dB SNR Off air modem signal (mel10)
- -5 dB SNR Analog SSB (mel12)
- -5dB SNR Codec 2 (ve9qrp_mel10)